## Slide 1: CS-773 Paper Presentation Improving the Utilization of Micro-operation Caches in x86 Processors Sumon Nath Hyperthreads(#6) sumon@cse.iitb.ac.in
Some of the figures are adapted and modified from the paper

## Slide 2: Coming up
Background - Micro op cache
Impact of Micro op cache
Motivation - Micro op cache inefficiency
Solutions proposed
Conclusion

## Slide 3: Background: CPU frontend

## Slide 4: Background: CPU frontend
Range of address ~ basic block

## Slide 5: Background: CPU frontend
Power hungry decoder -> Variable length ISA

## Slide 6: Background: CPU frontend
Fixed length micro-op(uop) -> simpler execution logic

## Slide 7: Background: CPU frontend
Uops cached into uop cache

## Slide 8: Background: CPU frontend
Hit uop cache -> bypass fetch & decode

## Slide 9: Prediction window(PW)
PW : can start and end anywhere in an I-cache line
Termination conditions
(1) I-cache line boundary (2) Predicted taken branch

## Slide 10: Uop cache entry

## Slide 11: Uop cache entry

## Slide 12: Uop cache entry

## Slide 13: Uop cache entry

## Slide 14: Uop cache entry
PW termination condition* -> uop cache entry written to uop cache
Uop cache entry: set of uops
Takeaway: uop cache entry may not occupy entire uop cache line
uop cache line
cache entry

## Slide 15: Impact of Uop cache
25%
40%

## Slide 16: Impact of Uop cache
Average UPC improvement: 11.2 % (64K uop cache)
Average reduction decoder power consumption: 39.2 %

## Slide 17: What next?
Throw money: Increase Uop cache size
Optimize the current Uop cache design

## Slide 18: Motivation: Inefficient uop cache
72% of Uop cache lines are highly fragmented
Main reason: termination conditions
*cache line size: 64B

## Slide 19: Fragmentation source: I-cache line boundary
Termination condition leads to smaller uop cache entries
Low uop cache utilization

## Slide 20: Fragmentation source: Predicted taken branch
Termination condition leads to smaller uop cache entries
Low uop cache utilization

## Slide 21: Fragmentation source: other conditions
Max. no. of immediate/displacement values per cache line
Max. no. of microcoded instructions per cache line

## Slide 22: Solutions proposed
Two solutions to reduce fragmentation:
CLASP - I-cache line boundary
Compaction - other termination cond.
            Replacement aware Compaction
            Prediction window aware Compaction
            Forced-PW aware compaction

## Slide 23: Pause
Any questions?

## Slide 24: Cache line boundary agnostic Uop (CLASP)
I-cache line
boundary
Sequential
code
(no branch)
Termination condition 1: I-cache line boundary

## Slide 25: Cache line boundary agnostic Uop (CLASP)
Merged
Relaxes I-cache line boundary termination condition
Only in case of sequential code
Doubles dispatch bandwidth

## Slide 26: Cache line boundary agnostic Uop (CLASP)
On average 35% of Uop cache entries are merged by CLASP

## Slide 27: Fragmentation source: Predicted taken branch
Termination condition 2

## Slide 28: Fragmentation source: Predicted taken branch
On average 49% of Uop cache entries terminated by predicted taken branches

## Slide 29: Compaction
Compacts Uop cache entries in a single cache line
Target termination conditions other than I-cache line boundary
Entries are not merged together to a single entry unlike CLASP
Dispatch bandwidth remains same unlike CLASP

## Slide 30: Compaction: Challenge
Which Uop cache entries to compact together?

## Slide 31: Replacement aware compaction(RAC)
MRU
Compacts new Uop cache entry with the MRU line in cache set
Ensures Uop cache entries are temporally correlated
Note: compaction at the time of Uop cache fill

## Slide 32: PW aware compaction (PWAC)
MRU
*Overrides RAC
Attempts to compact new Uop cache entry with entries from same Prediction window

## Slide 33: Forced-PWAC
T0

## Slide 34: Forced-PWAC
T0
T1
Forces compaction of entries from same PW

## Slide 35: Compaction technique distribution
Note: all 3 compaction techniques work simultaneously
Usage priority: PWAC > F-PWAC > RAC
Almost equal distribution

## Slide 36: Evaluation setup
Baseline Uop cache fits 2K uops

## Slide 37: Performance improvement
Performance improvement with CLASP + compaction: 5.3 %
5.3%

## Slide 38: Power reduction
Decoder power reduction with CLASP + compaction: 19.4 %
19.4%

## Slide 39: Conclusion
Uop cache is highly fragmented due to terminating conditions.
CLASP reduces fragmentation by relaxing I-cache line boundary termination condition
Compaction reduces fragmentation by joining possibly unrelated uop cache entries.

## Slide 40: Thank You Any Questions?

## Slide 41: Points to discuss
Why is PWAC prioritized over RAC compaction technique?
F-PWAC incurs an additional read and write
Compaction increases uop cache lookup latency