## Slide 1: CASPER @ IITB Effective Mimicry of Belady’s MIN Policy HPCA 2022 Sumon sumon@cse.iitb.ac.in

## Slide 2: Outline
Proposed solution - Mockingjay
Why it works?
Evaluation
Conclusion
Notes: ETA: Expected time of arrival

## Slide 3: Belady’s MIN Policy

## Slide 4: Belady’s MIN Policy

## Slide 5: Proposed method: Mockingjay
Emulate Belday’s MIN policy
Predicts Estimated time of arrival(ETA)
Evicts cache line with highest ETA
Notes: ETA: Expected time of arrival

## Slide 6: Mockingjay- example
Cache contents
Notes: ETA: Expected time of arrival

## Slide 7: Mockingjay- example
Cache contents
(insertion time)
Notes: ETA: Expected time of arrival

## Slide 8: ETA computation
Predicted Reuse Distance
Cache contents
ETA = Current time + predicted reuse distance
Notes: ETA: Expected time of arrival

## Slide 9: Reuse distance prediction
Reuse Distance Predictor
PC signature
LLC
ETA counters
Line address
Predicted reuse distance
ETA per cache line
Stores reuse distance per PC
How does RDP learns reuse distances?

## Slide 10: Training
Reuse Distance Predictor
Sampled Cache
Line address
Last Reuse distance
Last PC signature
Tracks the past reuse distance
Long history for few cache sets

## Slide 11
Any Questions

## Slide 12: Differentiating properties
Misprediction impact
Relative ordering of eviction
Delayed interpretation of ETA

## Slide 13: Under-predicted ETA
Add after every thing is done

## Slide 14: Prior work: Hawkeye
(Sampled Cache)
(RDP)
Prediction
Cache friendly
Cache averse
Binary classification

## Slide 15: Binary classification problem

## Slide 16: Binary classification problem
Misprediction -> global impact

## Slide 17: Mockingjay

## Slide 18: 1. Mockingjay - misprediction
Misprediction -> local impact

## Slide 19: 2. Relative eviction ordering

## Slide 20: Misprediction - Mockingjay
Relative order is correct for mispredicted ETA

## Slide 21: Relative ordering error
Ordering error on every misprediction
Low ordering error, even with high misprediction

## Slide 22: 3. Delayed interpretation of ETA
Eviction priority interpreted at eviction time instead of insertion time

## Slide 23: Scenario 1

## Slide 24: Scenario 2
Eviction order depends on ETA of all cache lines

## Slide 25: Evalution Methodology
Simulator: Champsim
33 memory-sensitive workloads from SPEC CPU2006, SPEC CPU2017 and GAP
Prefetcher used: IP-stride
Multicore
  Number of cores: 4
  100 mixes from the 33 workloads

## Slide 26: Speedup: single-core, no prefetching
Speedup of 5.5% over LRU close to 6% of MIN

## Slide 27: Speedup: single-core, with prefetching
Speedup of 3.6% over LRU compared to 2% with Harmony

## Slide 28: Speedup: 4-core
No prefetching: 15.2%, with prefetching: 13.3%
No prefetching
With prefetching

## Slide 29: Energy reduction
Reduces energy consumption by 9.1% compared to Hawkeye.

## Slide 30: Conclusion
Mockingjay mimics Belady’s MIN policy
Uses a ETA based approach instead of binary classification
Achieves performance close to MIN policy

## Slide 31: Acknowlegements
Some of the figures are taken from this paper and from the slides of Ishan Shah

## Slide 32
Thank You