## Slide 1: Seminar A study of Last-level cache management techniques, prefetching and their interactions Sumon Nath(21q050007) guided by Prof. Biswabandan Panda sumon@cse.iitb.ac.in

## Slide 2: Outline
Problem
LLC management techniques
Hardware prefetching
Prefetching techniques
Interaction between the two
Conclusion

## Slide 3: Problem
55% growth rate
10% growth rate
Notes: New plot

## Slide 4: Problem: Memory wall
CORE
DRAM Controller
100’s of cycles

## Slide 5: Latency tolerance techniques
Out-of-order execution
Multithreading
Caching
LLC Management techniques
Cache Prefetching

## Slide 6: Up next …
Problem
LLC management techniques
Hardware prefetching
Prefetching techniques
Interaction between the two
Conclusion

## Slide 7: LLC Management
Sets
Ways
…
A
B
D
C
Low priority
High priority
Eviction: Victim
Decisions:
Insertion - priority of new block
Promotion(hit) - updated priority
Last level cache
Priority chain

## Slide 8: Textbook: LRU
A
B
C
LRU
MRU
Insert : new block to MRU
A
D
Promote (on hit) : LRU to MRU
Evict: block at LRU position
A
B
D
C
LRU
MRU
C
D
Works only for cache friendly workloads
Assumption:
new block will be
re-referenced soon

## Slide 9: Access patterns
Recency friendly
, k < cache size
, k > cache size
Thrashing
Streaming
, k =∞
Scanning
(Non-temporal data)
Scan
LRU gets max. hits
Notes: Example of access patterns

## Slide 10: Access patterns
figure adapted from Prof. Biswa’s slides

## Slide 11: Re-reference interval prediction [ISCA ‘10]
A
B
D
C
RRP tail
RRP head
D
A
E
F
G
H
near-
immediate
intermediate
far
distant
Reuse
prediction
(0)
(1)
(2)
(3)
Insert : new block with RRPV=2/3
Promotion: update RRPV to 0
Eviction: block with RRPV=3
Assumption:
new block will not be
re-referenced soon

## Slide 12: RRIP variations
Static-RRIP
Insert with RRPV = 2
Discards scans quickly
Preserves cache friendly accesses
Bimodal-RRIP
Insert with RRPV=2/3 probabilistically
Preserves blocks in a thrashing workload
Scan resistant
Thrash resistant
Set-dueling
mechanism
Selects winning policy
Dynamic-RRIP: dynamically adapts to active workload

## Slide 13: SHiP [MICRO '11]
A
####
Signature
LLC
Signature history counter table
counter
Updates counter on hits
Predicts RRPV of new blocks with same signature
Improves RRIP accuracy by correlating blocks with same signature
PC
Memory region

## Slide 14: Problem with RRIP
Operate based on heuristics
Specific to certain workloads
Fail in case of more complex access patterns
Different approach: mimic Belady’s optimal policy

## Slide 15: Optimal technique - Belady

## Slide 16: Optimal technique - Belady
Goal: Evict block used furthest in future
Not practical

## Slide 17: Emulating Belady: Hawkeye [ISCA '17]
Emulates Belady’s MIN policy
Learns from OPTgen’s decisions
Prediction
Cache friendly
Cache averse
Binary classification
figure taken from Hawkeye paper

## Slide 18: Binary classification problem
Misprediction-> high impact
figure taken from Mockingjay paper

## Slide 19: Multiclass : Mockingjay [HPCA 2022]
Emulates Belady’s policy on past accesses
Predicts estimated time of arrival (ETA)
figure taken from Mockingjay paper

## Slide 20: Multiclass misprediction
Misprediction-> low impact
figure taken from Mockingjay paper

## Slide 21: Techniques employed
LLC Management techniques
Textbook
LRU
Intel
DRRIP
SHiP
Emulates Belady
Mockingjay
Hawkeye
Increasing complexity
Increasing performance
Notes: references

## Slide 22: Comparison of techniques (single core)
Belady
Mockingjay speedup - 5.5%, close to 6% of Belady’s optimal
figure taken from Mockingjay paper
Notes: references

## Slide 23
Comparison of techniques (4-core)
Mockingjay best performing technique with 15.2% speedup
figure taken from Mockingjay paper

## Slide 24: Up next …
Problem
LLC management techniques
Hardware prefetching
Prefetching techniques
Interaction between the two
Conclusion

## Slide 25: Hardware Prefetching
CORE
Cache
Prefetcher
X + 2
X + 1
X
X + 3
X + 3
data
X + 3
HIT
1
2
3
4
5

## Slide 26: Metrics of interest
Accuracy
  Used prefetches / total prefetches
Coverage
  Misses eliminated by prefetching / total misses
Timeliness
  How early/late a prefetch is?
DRAM bandwidth consumption
Cache pollution - unused prefetches

## Slide 27: Up next …
Problem
LLC management techniques
Hardware prefetching
Prefetching techniques
Interaction between the two
Conclusion

## Slide 28: Intel's Stride prefetching
Associates Instruction pointer(IP) to a constant stride

## Slide 29: Stride patterns
+1, +1, +1,…
+3, +3, +3,…
+1, +2, +1, +2…
+1, -3, +4, +1, +1, -3, +4, +1…
Constant Stride
Complex Stride

## Slide 30: Look-ahead based: SPP [MICRO 16]
Prefetch with P%
Lookahead prefetch(P’%)
Can handle more complex strides
Access
(signature)
+1, +3, +1, +3…
figure taken from SPP paper
Notes: Signature contains the strides

## Slide 31: Offset based: BOP [HPCA 16]
Trigger address
X
X + D
Prefetch address
Offset
D
Finds optimal offset D for prefetches
Dynamically updates D with changing app. behavior
Best offset learning
X
Recent prefetch requests
test di
If X-d present: increase confidence
Outcome: Timely prefetches
test di+1
Notes: Simple technique with very low hardware cost

## Slide 32: Region based: Bingo[HPCA 19]
100111011001
001100101000
100110110001
Spatial pattern
Records spatial access pattern over a memory region (eg. OS page)
Trigger access
PC
PC + address
PC + offset
Prefetch:
X+2
X+3
Pattern history table
…
Very aggressive in nature
Notes: Significant hardware overhead

## Slide 33: Prefetching techniques
Hardware prefetchers
Stride based
IP-stride
Lookahead based
VLDP
[MICRO ‘16]
SPP
[MICRO ‘16]
Region based
Bingo
[HPCA ‘19]
SMS
[ISCA ‘06]
Hybrid
IPCP
[ISCA ‘20]

## Slide 34: Comparison of prefetchers
As high as 31% improvement in single core system
Baseline: no prefetching
Notes: basline

## Slide 35: Up next …
Problem
LLC management techniques
Hardware prefetching
Prefetching techniques
Interaction between the two
Conclusion

## Slide 36: Interaction (More on RnD)
Cache
Management techniques
Prefetchers
Decides which blocks to retain
Decides which blocks to prefetch
Interact
Communicate

## Slide 37: Interaction (More on RnD)
Prefetch aware cache management [MICRO 2011]
  Modifies RRIP to adapt to prefetching
Kill the PC [ASPLOS 2017]
Co-operative prefetching & caching scheme
Harmony [ISCA 2018]
Modifies Belady’s optimal policy to accommodate prefetching

## Slide 38: Conclusion & future work
LLC management techniques are key to performance
Reached optimal performance threshold
Hardware prefetchers improves performance by many folds.
Need to study the interaction between the two to further improve performance, bandwidth, and energy consumption for single and multi-core systems

## Slide 39: Thank You Any Questions