## Slide 1
Do Not Forget Hardware Prefetchers While Mitigating Spectre Attacks
Sumon Nath (MS 2nd year) Adviser: Biswabandan Panda (IIT Bombay)
Executive Summary
Transient attacks (Spectre, Meltdown) are here to stay
Why?: Transient instructions get squashed by processor, but data brought by the transient instructions are in the cache
Solution: Do not cache the data of transient instructions
Problem: What about hardware prefetchers?
Solution: Designing Secure Prefetchers not at the cost of performance
Train and trigger hardware prefetching only for safe instructions
The Spectre Attack [S&P, 2019]
Big deal
References
GhostMinion(GM) cache
What does GM say?
If (x < array1_size)
y = array2[array1[x]]
Victim code
Mistrains
branch predictor
Invokes victim with out-of-bound x = 19
Secret key = array1[x] = 49
Attacker measures which location of array2 was brought into cache
49
129
Cache
array2[49]
L1D
L2
LLC
DRAM
CPU
GM
PF?
CORE
Cache
Prefetcher
X + 2
X + 1
X
X + 3
X + 3
data
X + 3
HIT
1
2
3
4
5
State-of-the-art solution [MICRO 2021]
Stores all speculative data
Writeback to L1D on commit
Wiped on context switch
Strictness ordering
Time guarding
Free slotting
Leap frogging
Hardware Prefetcher-101
Prefetch on commit 
Prefetch speculatively to GM cache 
Wiped on context switch 
Is it good enough in terms of performance?
20 to 50% performance degradation 
Intel improves performance/year by 2%  
Revisiting state-of-the-art prefetchers keeping performance and security in mind
Prefetcher should be at the GM cache or L1 cache?
How to trigger prefetcher on commit and provide same performance as the non-secure baseline?
Can we train prefetchers speculatively and still provide security guarantee?
[1] P. Kocher, et al. "Spectre attacks: Exploiting speculative execution." S&P 2019
[2] S. Pakalapati, and B. Panda "Bouquet of instruction pointers: Instruction pointer classifier-based spatial hardware prefetching." ISCA 2020
[3] S. Ainsworth "GhostMinion:
A strictness-ordered cache system for spectre mitigation." MICRO 2021
[4] A. Navarro-Torres, et al. "Berti:
an Accurate Local-Delta Data Prefetcher." MICRO 2022
Ongoing work
Chart: Speedup
| L0D speculative (GM) | L1D on-commit (GM) | L1D insecure (GM) | L1D (non-secure)
IP-stride | 0.87881 | 1.1429 | 1.1632 | 1.2929
IPCP | 0.57304 | 1.1705 | 1.1864 | 1.3521
Berti | 0.87942 | 1.2076 | 1.2294 | 1.3881
SPEC 2017 workloads
CASPER
Scan to download