## Slide 1: Quantifying Hardware Prefetching metrics of interest
MS R&D - 1
Sumon Nath
(21q050007)
sumon@cse.iitb.ac.in

## Slide 2: Topics to cover
Background on prefetchers & metrics of interest
Simulation software
Effect of lateness
Impact of DRAM bandwidth
Interaction with cache replacement policies

## Slide 3: Memory wall
55% growth rate
10% growth rate

## Slide 4: Memory wall
CORE
DRAM Controller
100’s of cycles

## Slide 5: Latency tolerance techniques
Out-of-order execution
Multithreading
Caching
Prefetching

## Slide 6: Hardware Prefetching
CORE
Cache
Prefetcher
X + 2
X + 1
X
X + 3
X + 3
data
X + 3
HIT
1
2
3
4
5

## Slide 7: Hardware prefetching
Idea
  Fetch the data before it is needed by program
  Latency hiding technique
Why?
  High memory latency up to 400 – 800 cycles
  Can eliminate Compulsory misses
  Reduces cache miss rate
  Reduces miss penalty
How?
  By observing/predicting the demand access patterns.

## Slide 8: State-of-the-art prefetchers
Bingo1
SPP2
IPCP3
[1] M. Bakhshalipour, M. Shakerinava, P. Lotfi-Kamran and H. Sarbazi-Azad, "Bingo Spatial Data Prefetcher," 2019 IEEE International Symposium on High Performance Computer Architecture (HPCA), 2019
[2] J. Kim, S. H. Pugsley, P. V. Gratz, A. L. N. Reddy, C. Wilkerson and Z. Chishti, "Path confidence based lookahead prefetching," 2016 49th Annual IEEE/ACM International Symposium on Microarchitecture (MICRO), 2016
[3] S. Pakalapati and B. Panda, "Bouquet of Instruction Pointers: Instruction Pointer Classifier-based Spatial Hardware Prefetching," 2020 ACM/IEEE 47th Annual International Symposium on Computer Architecture (ISCA), 2020.

## Slide 9: Prefetcher of interest: IPCP3
A bouquet of prefetchers
First IP prefetcher: Constant stride
Second IP prefetcher: Complex stride
Third IP prefetcher: Global stream
Fourth prefetcher: Next-line
Best performing prefetcher

## Slide 10: Metrics of interest
Accuracy
  Used prefetches / total prefetches
Coverage
  Misses eliminated by prefetching / total misses
Timeliness
  How early/late a prefetch is?
  Late prefetch

## Slide 11: Topics to cover
Background on prefetchers & metrics of interest
Simulation software
Effect of lateness
Impact of DRAM bandwidth
Interaction with cache replacement policies

## Slide 12: Simulation software – Champsim4
  Open source simulation software
  Trace-based simulator
  Trace: File that contains information about what the instructions perform and the number of cycles needed to complete their execution.
  Trace generated using – Pin Tool5
[4] https://github.com/ChampSim/ChampSim
[5] https://www.intel.com/content/www/us/en/developer/articles/tool/pin-a-dynamic-binary-instrumentation-tool.html

## Slide 13: Process of running Champsim
Program
PIN
Trace
Champsim
Results
Code to be run on Champsim
Simulation

## Slide 14: Topics to cover
Background on prefetchers & metrics of interest
Simulation software
Effect of lateness
Impact of DRAM bandwidth
Interaction with cache replacement policies

## Slide 15: What is a Late prefetch?
CORE
Cache
Prefetcher
Miss-status holding register (MSHR)
Enables multiple misses in parallel

## Slide 16: What is a Late prefetch?
CORE
Cache
Prefetcher
X + 2
X + 1
X
X + 3
X + 3
1
2
3
4
MSHR
X + 3 [P] |  |  | 
MISS
Late prefetch

## Slide 17: Lateness
Lateness - % of late prefetches
Why a problem?
  Accurate but late
  Cannot hide the whole memory latency
  Room for improvement
What happens if DRAM bandwidth is constrained?

## Slide 18: Lateness in IPCP [SPEC CPU benchmarks]
Chart: Benchmarks
| 600.perlbench_s-570B | 602.gcc_s-1850B | 602.gcc_s-2226B | 602.gcc_s-734B | 603.bwaves_s-1740B | 603.bwaves_s-2609B | 603.bwaves_s-2931B | 603.bwaves_s-891B | 605.mcf_s-1152B | 605.mcf_s-1536B | 605.mcf_s-1554B | 605.mcf_s-1644B | 605.mcf_s-472B | 605.mcf_s-484B | 605.mcf_s-665B | 605.mcf_s-782B | 605.mcf_s-994B | 607.cactuBSSN_s-2421B | 607.cactuBSSN_s-3477B | 607.cactuBSSN_s-4004B | 619.lbm_s-2676B | 619.lbm_s-2677B | 619.lbm_s-3766B | 619.lbm_s-4268B | 620.omnetpp_s-141B | 620.omnetpp_s-874B | 621.wrf_s-6673B | 621.wrf_s-8065B | 623.xalancbmk_s-10B | 623.xalancbmk_s-165B | 623.xalancbmk_s-202B | 628.pop2_s-17B | 641.leela_s-1083B | 649.fotonik3d_s-10881B | 649.fotonik3d_s-1176B | 649.fotonik3d_s-7084B | 649.fotonik3d_s-8225B | 654.roms_s-1007B | 654.roms_s-1070B | 654.roms_s-1390B | 654.roms_s-1613B | 654.roms_s-293B | 654.roms_s-294B | 654.roms_s-523B | 657.xz_s-2302B | Average
400 MT/s | 4.3 | 5.54 | 62.19 | 0.13 | 4.44 | 4.42 | 0.53 | 7.5 | 6.15 | 0.36 | 19.78 | 7.88 | 24.42 | 17.96 | 4.14 | 11.13 | 11.21 | 0.01 | 0 | 0 | 14.81 | 15.54 | 10.09 | 15.57 | 2.12 | 2.23 | 8.03 | 3.56 | 7.65 | 9.43 | 8.82 | 2 | 3.49 | 2.67 | 24.47 | 1.94 | 24.47 | 10.15 | 7.62 | 14.55 | 17.24 | 2.19 | 0.88 | 13.13 | 0.26 | 9.22
6400 MT/s | 1.7 | 0.5 | 0.81 | 0.03 | 0.21 | 0.22 | 0 | 0.33 | 4.89 | 0.38 | 17.15 | 2.62 | 22.12 | 15.05 | 3.44 | 9.63 | 9.83 | 0.01 | 0 | 0 | 7.02 | 8.71 | 0.48 | 8.77 | 1.41 | 1.58 | 2.09 | 0.42 | 4.64 | 1.37 | 1.05 | 0.42 | 2.04 | 1.49 | 0.63 | 0.02 | 0.63 | 0.82 | 1.53 | 2.03 | 1.91 | 0.08 | 0.04 | 1.04 | 0.21 | 3.1
lateness – 10 % on average (low bandwidth)
As high as 63%

## Slide 19: Expectation
If late prefetches eliminated (on-time)
  - Significant performance improvement

## Slide 20: Reality
Chart: Benchmark
| 600.perlbench_s-570B | 602.gcc_s-1850B | 602.gcc_s-2226B | 602.gcc_s-734B | 603.bwaves_s-1740B | 603.bwaves_s-2609B | 603.bwaves_s-2931B | 603.bwaves_s-891B | 605.mcf_s-1152B | 605.mcf_s-1536B | 605.mcf_s-1554B | 605.mcf_s-1644B | 605.mcf_s-472B | 605.mcf_s-484B | 605.mcf_s-665B | 605.mcf_s-782B | 605.mcf_s-994B | 607.cactuBSSN_s-2421B | 607.cactuBSSN_s-3477B | 607.cactuBSSN_s-4004B | 619.lbm_s-2676B | 619.lbm_s-2677B | 619.lbm_s-3766B | 619.lbm_s-4268B | 620.omnetpp_s-141B | 620.omnetpp_s-874B | 621.wrf_s-6673B | 621.wrf_s-8065B | 623.xalancbmk_s-10B | 623.xalancbmk_s-165B | 623.xalancbmk_s-202B | 628.pop2_s-17B | 641.leela_s-1083B | 649.fotonik3d_s-10881B | 649.fotonik3d_s-1176B | 649.fotonik3d_s-7084B | 649.fotonik3d_s-8225B | 654.roms_s-1007B | 654.roms_s-1070B | 654.roms_s-1390B | 654.roms_s-1613B | 654.roms_s-293B | 654.roms_s-294B | 654.roms_s-523B | 657.xz_s-2302B | Geomean
speedup | 1 | 1.0174 | 1.0497 | 1.0008 | 1.0119 | 1.0109 | 1 | 1.0009 | 1.0024 | 1.0004 | 1.0409 | 1.0001 | 1.0038 | 1.0084 | 1.0019 | 0.99083 | 1.0058 | 1.0007 | 1 | 1 | 1.0001 | 1 | 1 | 1.0001 | 1.0018 | 1.0022 | 1.0039 | 1.0016 | 1.0073 | 1.111 | 1.0888 | 1.0044 | 1.0002 | 1.0015 | 1.0018 | 1.0003 | 1.0017 | 1.0011 | 1.0038 | 1.0019 | 1.0035 | 1.0037 | 1.008 | 1.0036 | 1.0005 | 1.0086
DRAM BW: 400 MT/s
Fig: Performance improvement of IPCP when late prefetches are eliminated on SPEC2017 benchmarks
Geomean : 0.8 % improvement

## Slide 21: Why insignificant improvement?
Out-of-order
LOAD
2. SUB
3. LOAD
4. LOAD
5. MUL
LOAD
2. SUB
3. LOAD
4. LOAD
5. MUL
100 cycles
15 cycles
20 cycles
3 cycles
2 cycles
In-order Instruction Fetch
Out-of-order execution
In-order Commit

## Slide 22: Why insignificant improvement?
Out-of-order
LOAD
2. SUB
3. LOAD
4. LOAD
5. MUL
LOAD
2. SUB
3. LOAD
4. LOAD
5. MUL
20 cycles
15 cycles
20 cycles
3 cycles
2 cycles
In-order Instruction Fetch
Out-of-order execution
In-order Commit

## Slide 23
Issue Queue
Reorder Buffer
Commit
Execute
In-order
In-order
Out-of-order
F1 |  | Add .. | 
F0 |  | load … | 
ROB1
ROB2
ROB3
ROB4
ROB5
ROB6
ROB7
Issue queue
Reorder Buffer
Oldest
Newest
Why insignificant improvement?
ROB head
Actual ROB size : 350 entries

## Slide 24
Chart: Benchmark
| 600.perlbench_s-570B | 602.gcc_s-1850B | 602.gcc_s-2226B | 602.gcc_s-734B | 603.bwaves_s-1740B | 603.bwaves_s-2609B | 603.bwaves_s-2931B | 603.bwaves_s-891B | 605.mcf_s-1152B | 605.mcf_s-1536B | 605.mcf_s-1554B | 605.mcf_s-1644B | 605.mcf_s-472B | 605.mcf_s-484B | 605.mcf_s-665B | 605.mcf_s-782B | 605.mcf_s-994B | 607.cactuBSSN_s-2421B | 607.cactuBSSN_s-3477B | 607.cactuBSSN_s-4004B | 619.lbm_s-2676B | 619.lbm_s-2677B | 619.lbm_s-3766B | 619.lbm_s-4268B | 620.omnetpp_s-141B | 620.omnetpp_s-874B | 621.wrf_s-6673B | 621.wrf_s-8065B | 623.xalancbmk_s-10B | 623.xalancbmk_s-165B | 623.xalancbmk_s-202B | 628.pop2_s-17B | 641.leela_s-1083B | 649.fotonik3d_s-10881B | 649.fotonik3d_s-1176B | 649.fotonik3d_s-7084B | 649.fotonik3d_s-8225B | 654.roms_s-1007B | 654.roms_s-1070B | 654.roms_s-1390B | 654.roms_s-1613B | 654.roms_s-293B | 654.roms_s-294B | 654.roms_s-523B | 657.xz_s-2302B | Mean
<10 | 2.9851 | 7.4381 | 7.7392 | 38.5965 | 30.0903 | 29.1974 | 0 | 0.44514 | 13.1241 | 6.5238 | 4.3544 | 4.7001 | 2.2486 | 2.2297 | 12.9189 | 9.7633 | 38.4567 | 0 | 0 | 0 | 5.3846 | 4.9264 | 2.3866 | 5.0592 | 3.581 | 5.3122 | 7.3704 | 10.7198 | 5.6532 | 17.1909 | 17.1869 | 26.5176 | 23.8143 | 5.3576 | 0.12361 | 7.3826 | 0.34508 | 4.918 | 4.45 | 3.9031 | 3.8358 | 3.3445 | 18.3824 | 5.3792 | 32.797 | 10.3841
10-20 | 1.4925 | 47.933 | 16.7056 | 32.0175 | 10.1304 | 8.8626 | 0 | 1.0474 | 4.4966 | 32.6933 | 7.3788 | 7.4356 | 4.7274 | 6.5038 | 4.2993 | 5.2197 | 10.0455 | 33.3333 | 0 | 0 | 5.2176 | 5.0549 | 4.6142 | 5.2931 | 5.412 | 7.5966 | 8.737 | 17.5727 | 20.2941 | 11.4702 | 10.6625 | 26.5176 | 65.9939 | 6.4325 | 0.19778 | 13.4228 | 0.17254 | 5.3978 | 7.1044 | 4.8118 | 4.9099 | 27.7592 | 36.7647 | 6.5164 | 35.5198 | 13.7564
25-50 | 17.9104 | 27.6779 | 25.7152 | 8.3333 | 4.7141 | 5.3668 | 0 | 53.4171 | 13.1233 | 27.3152 | 13.9597 | 9.3885 | 9.4067 | 9.0341 | 11.3326 | 10.8526 | 20.2825 | 0 | 0 | 0 | 3.6405 | 3.5422 | 4.5346 | 3.5518 | 3.59 | 4.2247 | 7.8358 | 17.5345 | 21.1009 | 34.8651 | 31.1802 | 17.4121 | 1.3623 | 7.9788 | 0 | 17.4497 | 0.22184 | 12.7549 | 8.4143 | 8.3615 | 10.7403 | 10.3679 | 20.2206 | 7.6041 | 16.2129 | 12.9174
50-100 | 35.8209 | 15.7523 | 42.6142 | 5.7018 | 7.673 | 7.9271 | 0 | 31.3171 | 16.5994 | 5.5373 | 25.6899 | 17.8374 | 19.316 | 19.329 | 15.1622 | 17.9858 | 2.9136 | 0 | 0 | 0 | 5.9598 | 6.1205 | 7.3986 | 6.1252 | 7.0903 | 7.5575 | 11.8976 | 18.3002 | 19.8766 | 27.1173 | 28.902 | 8.3866 | 6.0545 | 12.6983 | 0.074166 | 16.7785 | 0.12324 | 18.1128 | 12.5173 | 16.9405 | 19.1408 | 11.3712 | 9.9265 | 12.9338 | 3.4653 | 13.8582
100-500 | 41.791 | 1.1987 | 7.2257 | 15.3509 | 47.2919 | 48.646 | 0 | 13.7732 | 52.5738 | 27.8456 | 48.4333 | 54.0372 | 63.9825 | 62.3823 | 56.1889 | 56.0156 | 28.2924 | 66.6667 | 0 | 0 | 53.3566 | 53.7055 | 63.564 | 53.3005 | 80.3267 | 75.309 | 52.2869 | 34.8009 | 33.0751 | 9.3565 | 12.0683 | 21.1661 | 2.775 | 66.9924 | 99.6044 | 42.953 | 99.1373 | 56.3375 | 56.6794 | 61.082 | 58.8416 | 40.4682 | 14.7059 | 64.3924 | 12.005 | 45.4759
>500 | 0 | 0 | 0 | 0 | 0.1003 | 0 | 0 | 0 | 0.082745 | 0.084863 | 0.18387 | 6.6012 | 0.31894 | 0.52119 | 0.098118 | 0.16294 | 0.0092293 | 0 | 0 | 0 | 26.4408 | 26.6506 | 17.502 | 26.6702 | 0 | 0 | 11.8722 | 1.072 | 0 | 0 | 0 | 0 | 0 | 0.54035 | 0 | 2.0134 | 0 | 2.479 | 10.8345 | 4.9012 | 2.5316 | 6.689 | 0 | 3.1741 | 0 | 3.608
Lateness by # of cycles
cycles
Fig: Percent of late prefetches by # of cycles of IPCP on SPEC2017 benchmarks
< 4% of late prefetches are late by > 500 cycles

## Slide 25: Topics to cover
Background on prefetchers & metrics of interest
Simulation software
Effect of lateness
Impact of DRAM bandwidth(BW)
Interaction with cache replacement policies

## Slide 26: Why care about DRAM BW?
Servers – Multicore system
  32 cores
  DRAM BW per channel – 3200 MT/s
  4 available channels
  1 channel for 8 cores
  On average per core DRAM BW
      – 400 MT/s(3.2 GB/s)

## Slide 27: Why care about DRAM BW?
Non volatile memory – Intel Optane
Fastest NVMs
read – 3 GB/s = 375 MT/s
write – 1 GB/s = 125 MT/s

## Slide 28: IPCP performance(high DRAM BW)
Overall improvement: 35 %
Fig: Performance improvement with IPCP on SPEC2017 benchmarks compared to no prefetching baseline

## Slide 29: IPCP performance(low DRAM BW)
Overall improvement: 10 %
Fig: Performance improvement with IPCP on SPEC2017 benchmarks compared to no prefetching baseline

## Slide 30: Impact of DRAM BW on performance
Chart: Dram Bandwidth
| 6400 MT/s | 1600 MT/s | 800 MT/s | 400 MT/s | 200 MT/s
Normalized IPC | 1.35 | 1.33 | 1.23 | 1.1 | 0.97
Significant performance drop as DRAM BW decreases
Performance degradation in case very low DRAM BW
NOPE6
  Turn OFF prefetching when performance degrades with low DRAM BW
[6] Anuj Mishra and Biswabandan Panda, “Hardware Prefetcher Aggressiveness Controllers: Do We Need Them All the Time?”, ASPLOS 2021, Workshop on Negative results, Opportunities, Perspectives, and Experiences

## Slide 31: Impact on prefetcher coverage
Fig: Comparison of prefetcher coverage at the L1D with IPCP on SPEC2017 benchmarks for low & high DRAM BW
Coverage drops from 61 % to 53 %.
Chart: Benchmarks
| 600.perlbench_s-570B | 602.gcc_s-1850B | 602.gcc_s-2226B | 602.gcc_s-734B | 603.bwaves_s-1740B | 603.bwaves_s-2609B | 603.bwaves_s-2931B | 603.bwaves_s-891B | 605.mcf_s-1152B | 605.mcf_s-1536B | 605.mcf_s-1554B | 605.mcf_s-1644B | 605.mcf_s-472B | 605.mcf_s-484B | 605.mcf_s-665B | 605.mcf_s-782B | 605.mcf_s-994B | 607.cactuBSSN_s-2421B | 607.cactuBSSN_s-3477B | 607.cactuBSSN_s-4004B | 619.lbm_s-2676B | 619.lbm_s-2677B | 619.lbm_s-3766B | 619.lbm_s-4268B | 620.omnetpp_s-141B | 620.omnetpp_s-874B | 621.wrf_s-6673B | 621.wrf_s-8065B | 623.xalancbmk_s-10B | 623.xalancbmk_s-165B | 623.xalancbmk_s-202B | 628.pop2_s-17B | 641.leela_s-1083B | 649.fotonik3d_s-10881B | 649.fotonik3d_s-1176B | 649.fotonik3d_s-7084B | 649.fotonik3d_s-8225B | 654.roms_s-1007B | 654.roms_s-1070B | 654.roms_s-1390B | 654.roms_s-1613B | 654.roms_s-293B | 654.roms_s-294B | 654.roms_s-523B | 657.xz_s-2302B | Average
6400 MT/s | 23.7 | 91.16 | 96.12 | 95.19 | 94.88 | 94.91 | 92.75 | 98.02 | 20.23 | -8.12 | 53.92 | 48.15 | 26.63 | 29.82 | 18.1 | 20.73 | 3.72 | -0.05 | -0.25 | -0.19 | 70.31 | 66.28 | 96.07 | 66.25 | 2.63 | 4.43 | 87.27 | 83.72 | 13.95 | 94.93 | 95.21 | 84.5 | 37.51 | 70.93 | 96.8 | 98.16 | 96.79 | 95.79 | 95.15 | 92.72 | 94.04 | 96.29 | 90.39 | 95.55 | 0.46 | 60.5678
400 MT/s | 21.2 | 85.71 | 30.9 | 95.09 | 90.88 | 90.93 | 91.23 | 90.97 | 18.86 | -8.4 | 43.42 | 42.95 | 24.04 | 26.54 | 17.31 | 19.33 | 2.31 | 0.01 | -0.24 | -0.19 | 64.02 | 61.87 | 78.35 | 61.64 | 1.95 | 3.81 | 79.48 | 78.4 | 11.93 | 86.39 | 87.04 | 82.57 | 36.13 | 69.37 | 73.42 | 95.92 | 73.43 | 78.35 | 86.95 | 74.98 | 77.97 | 89.27 | 89.43 | 80.6 | 0.4 | 53.4782
DRAM BW:

## Slide 32: Impact on prefetcher accuracy
Fig: Comparison of prefetcher accuracy at the L1D with IPCP on SPEC2017 benchmarks for low & high DRAM BW
Chart: Benchmarks
| 600.perlbench_s-570B | 602.gcc_s-1850B | 602.gcc_s-2226B | 602.gcc_s-734B | 603.bwaves_s-1740B | 603.bwaves_s-2609B | 603.bwaves_s-2931B | 603.bwaves_s-891B | 605.mcf_s-1152B | 605.mcf_s-1536B | 605.mcf_s-1554B | 605.mcf_s-1644B | 605.mcf_s-472B | 605.mcf_s-484B | 605.mcf_s-665B | 605.mcf_s-782B | 605.mcf_s-994B | 607.cactuBSSN_s-2421B | 607.cactuBSSN_s-3477B | 607.cactuBSSN_s-4004B | 619.lbm_s-2676B | 619.lbm_s-2677B | 619.lbm_s-3766B | 619.lbm_s-4268B | 620.omnetpp_s-141B | 620.omnetpp_s-874B | 621.wrf_s-6673B | 621.wrf_s-8065B | 623.xalancbmk_s-10B | 623.xalancbmk_s-165B | 623.xalancbmk_s-202B | 628.pop2_s-17B | 641.leela_s-1083B | 649.fotonik3d_s-10881B | 649.fotonik3d_s-1176B | 649.fotonik3d_s-7084B | 649.fotonik3d_s-8225B | 654.roms_s-1007B | 654.roms_s-1070B | 654.roms_s-1390B | 654.roms_s-1613B | 654.roms_s-293B | 654.roms_s-294B | 654.roms_s-523B | 657.xz_s-2302B | Average
6400 MT/s | 32.418 | 82.3335 | 90.9077 | 86.2199 | 94.6633 | 94.4906 | 97.9825 | 99.6631 | 25.3508 | 3.819 | 39.3098 | 49.1189 | 27.0511 | 28.4558 | 25.8259 | 22.8315 | 13.5291 | 8.8069 | 19.3722 | 24.1336 | 92.9303 | 91.2419 | 99.52 | 91.1714 | 13.6991 | 13.8631 | 78.0974 | 66.4191 | 17.9585 | 88.569 | 90.7487 | 73.8643 | 58.3236 | 58.437 | 98.819 | 93.0917 | 98.8797 | 93.247 | 93.7184 | 90.1671 | 91.5975 | 95.989 | 90.0125 | 93.0429 | 11.9169 | 63.3691
400 MT/s | 29.7889 | 77.3443 | 29.5822 | 86.1808 | 25.7397 | 25.3 | 94.4014 | 92.4997 | 24.0856 | 3.5599 | 34.6777 | 43.934 | 24.6072 | 25.522 | 25.1191 | 21.3608 | 12.1519 | 1.0211 | 19.8651 | 24.1767 | 85.1675 | 84.4291 | 89.9116 | 84.3885 | 12.9901 | 13.2202 | 52.1803 | 60.1239 | 15.4172 | 81.3293 | 82.9773 | 62.6101 | 56.8053 | 57.3887 | 74.9973 | 19.3853 | 75.0562 | 40.5119 | 47.2936 | 57.5226 | 76.1026 | 81.6678 | 88.7457 | 60.7102 | 11.8591 | 48.7491
Accuracy drops from 63.5 % to 48 %.
Less useful prefetches
Lot of scope for improvement in case of constrained DRAM bandwidth

## Slide 33: Topics to cover
Background on prefetchers & metrics of interest
Simulation software
Effect of lateness
Impact of DRAM bandwidth
Interaction with cache replacement policies

## Slide 34: Why cache replacement policies?
Prefetchers – brings in cache block
Replacement policies – evicts a cache block
Must work in unison to improve performance
State-of-art prefetchers - No interaction

## Slide 35: Cache replacement policies used
Re-Reference Interval Prediction(RRIP7)
  Static RRIP (SRRIP7)
  Dynamic RRIP (DRRIP7)
Prefetch-Aware Cache Management (PACMAN8)
[7] Aamer Jaleel, Kevin B. Theobald, Simon C. Steely, and Joel Emer, “High performance cache replacement using re-reference interval prediction (RRIP)”, ISCA’10
[8] C. Wu, A. Jaleel, M. Martonosi, S. C. Steely and J. Emer, "PACMan: Prefetch-Aware Cache Management for high performance caching," 2011 44th Annual IEEE/ACM International Symposium on Microarchitecture (MICRO), 2011

## Slide 36
IPCP performance(client-server)- L1
Fig: Performance improvement of IPCP with different cache replacement policies at the L1 compared to a baseline with LRU policy
No significant performance improvement

## Slide 37
IPCP performance(client-server)- L2C
Fig: Performance improvement of IPCP with different cache replacement policies at the L2C compared to a baseline with LRU policy
Significant performance improvement across server benchmarks
Max. improvement for Pacman – 7.5 %
On Average – 2.5 % improvement for Pacman

## Slide 38
IPCP performance(client-server)- LLC
Max. improvement for Pacman – 5.5 %
On Average – 1 % improvement for Pacman
Fig: Performance improvement of IPCP with different cache replacement policies at the LLC compared to a baseline with LRU policy

## Slide 39: Champsim code
Already Implemented:
IPCP
Identification of late prefetches
SRRIP, DRRIP
Implementations for R&D work:
Elimination of late prefetches
Lateness by # of cycles
Pacman

## Slide 40: Conclusion & future work
Lateness is not an issue for IPCP, but needs further study.
Significant performance degradation for low dram bandwidth
Replacement policies play a crucial role on prefetcher performance
Cache pollution – in progress

## Slide 41: Acknowledgements
Some of the slides are adapted and modified from Prof. Biswabandan Panda, Prof. Onur Mutlu and my senior Rajiv.

## Slide 42: Thank You