## Slide 1: CS305: Computer Architecture
Branch Prediction
https://www.cse.iitb.ac.in/~biswa/courses/CS305/main.html

## Slide 2: Branch instructions
I1:
I2:
I3:
I4:
I5:
t1
t2
t3
t4
t5
t6
t7
t8
Time:
Inst
I6:
IF (Fetch)
ID (Decode)
EX (ALU)
MEM
WB
IF
ID
IF
EX
ID
IF
MEM
WB
EX stage computes if branch is taken
If branch is taken, these instructions MUST NOT complete!
I-Mem

## Slide 3: Branch Predictors
I1:
I2:
I3:
I4:
I5:
t1
t2
t3
t4
t5
t6
t7
t8
Time:
Inst
I6:
IF (Fetch)
ID (Decode)
EX (ALU)
MEM
WB
IF
ID
IF
EX
ID
IF
MEM
WB
EX stage computes if branch is taken
If branch is taken, these instructions MUST NOT complete!
I-Mem
A control instr?
Taken or Not Taken?
If taken, where to? What PC?
Branch Predictor
Predictions

## Slide 4: A quick recap
What if PC=PC+4? Not TRUE
Flush/kill all the instructions in the wrong path.

## Slide 5: Branch Prediction: 10K Feet View
Predict whether the next PC is a branch PC, at the fetch stage?

## Slide 6: Branch Prediction: 10K Feet View
Predict whether the next PC is a branch PC, at the fetch stage?
If branch, will it be taken?

## Slide 7: Branch Prediction: 10K Feet View
Predict whether the next PC is a branch PC, at the fetch stage?
If branch, will it be taken?
If taken, what is the target address?

## Slide 8: Branch Prediction: 10K Feet View
Predict whether the next PC is a branch PC, at the fetch stage?
If branch, will it be taken?
If taken, what is the target address?
How?

## Slide 9: Branch Prediction: 10K Feet View
Predict whether the next PC is a branch PC, at the fetch stage?
If branch, will it be taken?
If taken, what is the target address?
How?
We know whether it is a branch PC or not in the decode stage. Oh no 

## Slide 10: Branch Predictor: A bit deeper
Three tasks
Is the PC a branch/jump? YES/NO
If Yes, can we predict the direction? Taken or not-taken
If taken, can we predict the target address?

## Slide 11: Let’s see
Program
Counter
Address of the
current branch

## Slide 12: Let’s see
Direction predictor
Program
Counter
PC + 4
taken?
Next Fetch
Address
Address of the
current branch

## Slide 13: Let’s see
target address
Direction predictor
Repository of Target Addresses (BTB: Branch Target Buffer)
Program
Counter
PC + 4
taken?
Next Fetch
Address
hit?
Address of the
current branch

## Slide 14: Static (compiler) Direction Prediction Techniques
Always not-taken: Simple to implement: no need for BTB,
no direction prediction
Low accuracy: ~30-40%
Always taken: No direction prediction, we need BTB though
Better accuracy: ~60-70%
Backward branches (i.e., loop branches) are usually taken

## Slide 15: Dynamic Predictors
Microarchitectural way of predicting it.
Simple one: Last time predictor

## Slide 16: Last-time predictor
predict
taken
predict
not
taken
actually
taken
actually
not taken

## Slide 17: Last-time predictor
predict
taken
predict
not
taken
actually
not taken
actually
taken
actually
taken
actually
not taken

## Slide 18: Implementation
K bits of branch instruction address
Index

## Slide 19: Implementation
K bits of branch instruction address
Index
Branch history table of 2K entries, 1 bit per entry

## Slide 20: Implementation
K bits of branch instruction address
Index
Branch history table of 2K entries, 1 bit per entry
Use this entry to predict this branch:
0: predict not taken
1: predict taken

## Slide 21: Performance of Last-time predictor
TTTTTTTTTTNNNNNNNNNN - 90% accuracy
Always mispredicts the last iteration and the first iteration of a loop branch
Accuracy for a loop with N iterations = (N-2)/N
+ Loop branches for loops with large number of iterations
-- Loop branches for loops will small number of iterations

## Slide 22: Performance contd.
TNTNTNTNTNTNTNTNTNTN  0% accuracy
20% of all instructions are branches, 85% accuracy
Last-time predictor CPI =
[ 1 + (0.20*0.15) * 2 ] =
1.06

## Slide 23: 2-bit Predictors: A bit better
pred
taken
pred
taken
pred
!taken
pred
!taken
actually
taken
actually
taken
actually
!taken
actually
!taken
actually
!taken
actually
!taken
actually
taken
actually
taken
“weakly
taken”
“strongly
taken”
“weakly
!taken”
“strongly
!taken”

## Slide 24: 感謝