## Slide 1: CS305: Computer Architecture
Tutorial-I
https://www.cse.iitb.ac.in/~biswa/courses/CS305/main.html

## Slide 2: Problem-1
Consider the unpipelined processor that has a 1 ns clock cycle and that it uses 4 cycles for ALU operations and branches and 5 cycles for memory operations. Assume that the relative frequencies of these operations are 40%, 20%, and 40%, respectively. Suppose that pipelining the processor adds 0.2 ns of overhead to the clock. Ignoring any latency impact, how much speedup in the instruction execution rate will we gain from a pipeline?

## Slide 3: Solution
The average instruction rate (execution time) on the unpipelined processor =
Clock cycle X Average CPI
= 1 ns X [(40% + 20%)X 4 + 40% X 5]
= 1 ns X 4.4 = 4.4 ns

## Slide 4: Solution Contd.
In the pipelined processor,
Clock cycle time = 1ns + 0.2ns latch overhead = 1.2ns
Speedup = 4.4/1.2 = 3.66 times
tips: The question does not mention #pipeline stages. If you think deep, it does not matter because after a while one instruction will be done in one cycle, so speedup is just the ratio of cycle time

## Slide 5: Problem-2
Consider a 4-stage pipelined CPU with the following details in terms of #cycles: I1 to I4 are four instructions
 | Stage-1 | Stage-2 | Stage-3 | Stage-4
I1 | 2 | 1 | 1 | 1
I2 | 1 | 3 | 2 | 2
I3 | 2 | 1 | 1 | 3
I4 | 1 | 2 | 2 | 2
How many cycles will it take to execute (i) I1 to I4 once (ii) I1 to I4 twice

## Slide 6: Try it on your own for two iterations (I1 to I4 twice)
The answer will be 23

## Slide 7: Solution (Make sure no two instructions use the same stage at the same time)

## Slide 8: Problem 3
Consider a datacenter processor running at 100% utilization at 100 W, 50% of the power is attributed to leakage. What is the total power dissipation when the processor is running at 25% utilization?
Total power =
dynamic power + leakage power
50W x 25% + 50W = 62.5W

## Slide 9: Problem 4
Your laptop has an IPC that is 30% worse than your friend’s laptop. It has a clock speed that is 40% higher than friend’s laptop. If the ISA and the compiler used are the same, what is the speedup with your laptop compared to your friend’s laptop?

## Slide 10: Solution
Speed up = Your laptop’s performance
----------------------------------
Your friend’s laptop’s performance
Execution time = cycle time X CPI X #Instructions
Performance = 1/execution time
= clock speed X IPC/instructions

## Slide 11: Solution Contd.
Speedup = Yours (clock speed X IPC)
-------------------------------------------
Your Friend’s (clock speed X IPC)
= 1.4 X 0.7
= 0.98