## Slide 1: CS305: Computer Architecture
Tutorial - $$$
https://www.cse.iitb.ac.in/~biswa/courses/CS305/main.html

## Slide 2: Problem-1
Consider a 4-way set associative cache consisting of 128 lines with a line size of 64 bytes. The CPU generates a 20-bit physical address . Find the number of bits in the TAG, INDEX and BYTE fields.

## Slide 3: Solution
Number of sets = # of lines in cache/associativity
= 128/4 = 32 = 25
Block size = 26 Bytes
Address bits:
tag | index | Byte offset

## Slide 4: Problem-2
How many total bits are required for a direct-mapped cache with 16 KB of data and 16 B blocks, assuming a 32-bit address?

## Slide 5: Solution
Data in cache = 16 KB = 214 B
Block size = 24 B
# of cache lines = 214/24 = 210
Address bits:
Total cache size = 214 * 8 + 210(18 + 1) bits = 147 Kbits
tag | index | Byte offset

## Slide 6: Problem-3
Consider a direct-mapped cache with 64 blocks and a block size of 16 bytes. To what block number does byte address 2000 map?
Also find the set number to which the address will be mapped to, in case the cache is set associative with an associativity of 4.

## Slide 7: Solution
  Direct-mapped:
  Block address = byte address / bytes per address
  = 2000/16
  = 125
  Block # = (block address) mod (# of blocks in cache)
  = 125 mod 64
  = 61

## Slide 8: Solution
  Set associative:
  # of sets in cache = 64/4 = 16 sets
  set # = (block address) mod (# of sets in cache)
  = 125 mod 16
  = 13

## Slide 9: Problem-4
Assume the miss rate of an instruction cache is 2% and the miss rate of the data cache is 4%. If a processor has a CPI of 2 without any memory stalls and the miss penalty is 100 cycles for all misses, determine how much faster a processor would run with a perfect cache that never missed. Assume the frequency of all loads and stores is 36%.

## Slide 10: Solution
Instruction miss cycles = IC x 0.02 x 100 = 2 IC (IC = instruction count)
Data miss cycles = IC x 0.36 x 0.04 x 100 = 1.44 IC
Total # of memory stall cycles = (2 + 1.44) IC = 3.44 IC
CPI including memory stalls = 2 + 3.44 = 5.44
speedup = CPU time with stalls / CPU time with perfect cache
= IC x CPIstall x clock / IC x CPIperfect x clock
= CPIstall/CPIperfect = 5.44/2 = 2.72

## Slide 11: Problem-5
Consider a 2-way set associative cache with 256 blocks and uses LRU replacement. Initially the cache is empty.
The following sequence of access to memory blocks:
{0, 128, 256, 128, 0, 128, 256, 128, 1, 129, 257, 129, 1, 129, 257, 129}
is repeated 10 times.
Find the number of compulsory and conflict misses for the cache.

## Slide 12: Solution
1st iteration:
Compulsory misses = 6
Conflict misses = 4
For each subsequent iteration:
Compulsory misses = 0
Conflict misses = 8
Total compulsory misses = 6
Total conflict misses = 4 + 8*9 = 76

## Slide 13: Problem-6
Consider a system with 2 level cache. Access times of Level 1 cache, Level 2 cache and main memory are 1 ns, 10 ns, and 500 ns respectively. The hit rates of Level 1 and Level 2 caches are 0.8 and 0.9, respectively. Find out the average memory access time of the system.

## Slide 14: Solution
Assume,
L1 access time = t1 L1 hit rate = h1
L2 access time = t2 L2 hit rate = h2
Mem. Access time = tm
AMAT = t1 + (1 – h1 )( t2 + ( 1 – h2 ) tm )
= t1 + (1 – h1 ) t2 + ( 1 – h1 )( 1 – h2 ) tm
= 1 + 0.2 x 0.9 x 10 + 0.2 x 0.1 x 500 = 13 ns